## Slide 1: A Data-Driven Approach Towards NIF Neutron Time-of-Flight Diagnostics Using Machine Learning and Bayesian Inference
Su-Ann Chong
Summer Internship Final Wrap-up
Dave Schlossberg, Jim Gaffney, Luc Peterson, Kelli Humbird
August 13, 2021

## Slide 2: Outline
Background
  Neutron time-of-flight (nToF) diagnostics
  nToF physics-driven approach
  Motivation
Approaches
  Approach overview and project scope
  Data generation using physics model (Ballabio)
  Surrogate model for data generation using machine learning (DJINN)
  Posterior distribution approximation using Bayesian inference (MCMC)
Summary
  Work accomplished
  Future work

## Slide 3: Background: Neutron Time-of-Flight (nToF) Diagnostics
Neutron time-of-flight (nToF) diagnostics
  is an essential tool for diagnosing implosions at the NIF.
  analyzes the nToF spectrum produced from the fusion reactions to provide important details of the performance of the implosion:
    neutron yield
    (DT reaction, DD reaction)
    ion temperature
    down-scatter ratio (DSR)

## Slide 4: Background: nToF Physics-Driven Approach
The neutron time-of flight spectrum:
  From target chamber to nToF detector
  With a known distance and time-of-flight, neutron energy can be calculated.
The fit function1:
The Ballabio distribution2:
[1] R. Hatarik et al J. Appl. Phys. 118, 184502 (2015) [[2] L. Ballabio et al 1998 Nucl. Fusion 38 1723

## Slide 5: Background: Problem Statement
Motivation behind using data-driven approaches:
  To complement the power of physics modeling and simulations
  To provide more insights about the underlying physics in complex systems
Goal:
  To approximate the probability distributions of fusion quantities
  To quantify correlation between fusion quantities
Big picture:
  Provide more information for nToF diagnostics to help ICF experiments to achieve higher performing implosions

## Slide 6: Approaches: Project Scope
Due to the complexity of the problem, we are narrowing down our problem to start out:
  DT reactions (DD reaction excluded)
  North pole detector (NTOF-21M-SPEC-NP)
  Detector #4
  Shots from 2017 – 2021
Data generation routine
  31 DT shots that have nToF analysis from 2017 – 2021
  Took the fitted Ballabio model to generate scope traces by specifying model parameters and initial conditions
  Validated the model with experimental measurements.

## Slide 7: Approaches: RoadMap
Prior probability of fusion quantities
Form a Likelihood function
Compare to observations
Accept/reject
algorithm
Generated by a surrogate ML model
(DJINN) [1]
--------- OR ----------
Generated by modeling [2,3]
Running simulation models can be computationally expensive
[1] K. Humbird, et al 2019. IEEE Transactions on Neural Networks and Learning Systems, 30(5), 1286–1295.
[2] R. Hatarik et al J. Appl. Phys. 118, 184502 (2015)
[3] L. Ballabio et al 1998 Nucl. Fusion 38 1723
Bayesian inference (MCMC) (#3)
Data generation using physics model (#1)
Data generation using ML model (#2)

## Slide 8: Approaches: Data Generation
Using the Ballabio fit model routine, 10,000 data points are generated using a single shot --- N210605-001-999.
  instrument response function (IRF)
  detector sensitivity
  beam attenuation factors
  model parameters:
    Random sampling using Latin hypercube sampling
Different shots (taken at different time) may have different IRFs, detector sensitivities and beam attenuation factors due to instrument modifications or performance degradation over time.
 | Lower bound | Upper bound
Neutron yield, |  | 
Ion temperature , |  | 
Down-scattered ratio, |  | 
 | Lower bound | Upper bound

## Slide 9: Approaches: Surrogate Model Data Generation Using DJINN
Deep Jointly Informed Neural Network (DJINN)
Network architecture
Evaluation
Hyperparameters | Values
Number of tree | 1
Depth of tree | 6
Metric | Value
Mean square error | 
Mean absolute error | 
Explained variance score | 
Metric | Value
Mean square error | 
Mean absolute error | 
Explained variance score | 
Speedup achieve: x1000
Surrogate model: ~1ms Ballabio fit model: ~1s

## Slide 10: Approaches: Approximate Posterior Probability Using MCMC
MCMC Parameters | Values
Framework | PyMC3 + Theano
Prior probability distribution | Normal distribution Uniform distribution
Likelihood function | DJINN surrogate model
Sampling method | No U-Turn Sampler (NUTS)
Multiprocessing | 4
Number of iterations | 3,000 (x4)
Number of burn samples | 1,000 (x4)
Execution time | ~ 1.5 mins
Markov Chain Monte Carlo
  Based on Bayes theorem
  Combination of Markov Chain and Monte Carlo
  Random sampling from distributions such that the current state is probabilistically dependent on the previous state

## Slide 11: Summary: Preliminary Results From MCMC
 | Ground truth | 2.5% quantile | 16% quantile | 50% quantile | 84% quantile | 97.5% quantile
 | 4 |  |  |  |  | 
 | 8 |  |  |  |  | 
 | Ground truth | 2.5% quantile | 16% quantile | 50% quantile | 84% quantile | 97.5% quantile
Currently, result reported
are performed on
test data without noise.
Accurate modeling of signal noise is needed before it can be performed on experimental data

## Slide 12
Disclaimer
This document was prepared as an account of work sponsored by an agency of the United States government. Neither the United States government nor Lawrence Livermore National Security, LLC, nor any of their employees makes any warranty, expressed or implied, or assumes any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, apparatus, product, or process disclosed, or represents that its use would not infringe privately owned rights. Reference herein to any specific commercial product, process, or service by trade name, trademark, manufacturer, or otherwise does not necessarily constitute or imply its endorsement, recommendation, or favoring by the United States government or Lawrence Livermore National Security, LLC. The views and opinions of authors expressed herein do not necessarily state or reflect those of the United States government or Lawrence Livermore National Security, LLC, and shall not be used for advertising or product endorsement purposes.